## Slide 1: EMI Noise Impedance
Quick Overview
Abel Keeley
Electronics EEDP | Clothes Care
GE Appliances, a Haier company

## Slide 2
Background - Theoretical
EMI
DM
CM
Disturbance in electrical circuit due to outside source[s] of electromagnetic energy.
Common Mode (CM) noise flows to ground (displacement current). Caused by coupling through parasitic capacitance
Differential Mode (DM) noise flows between two lines. Caused by coupling through parasitic inductance, typically trace loops, harnesses, etc.
Notes: Source: Advanced EMI, B1 class slides @ Global Edison Program - Lecture Material - All Documents (sharepoint.com)

## Slide 3
Background - Measurements
What we want from a measurement setup:
Isolates the Equipment Under Test (EUT) from existing noise on the grid (while still powering it)
Capable of measuring high frequency signals on L and N
A Line Impedance Stabilization Network (LISN) and a Spectrum Analyzer will accomplish both!
We don’t want to just measure noise on L and N though, we want CM/DM noise.
  The equations , still hold for AC systems.
  Can use and power combiners to add and subtract complex RF signals…
Notes: Sources: “EMI: Theory, Issues, and Solutions” -> EMITrainingSlides.pdf @ Electronics Hardware Portal - Historic Presentations - All Documents (sharepoint.com), “New EMI Filter Design Methods for DC-DC and AC-DC Switching Power Supplies”.

## Slide 4
Background – Circuit Analysis
This circuit representation, while correct, is not particularly helpful for considering EMI performance.
CM Eqv. Circuit
DM Eqv. Circuit

## Slide 5
Motivation
Want our appliances to meet FCC Part A conducted emission limits.
  Not a legal requirement, as most digital appliances are exempt from these limits.
To try and meet these requirements, some form of filter is often required.
  Due to the complexity of EMI filter design, older designs are often recycled with minor tweaks
  This strategy generally entails much iteration, guided by significant amounts of manual testing.
  A design methodology that would reduce the number of iterations would help drive better designs
FCC Conducted Emissions Limits
Conducted Emissions Results for Current Production PTW600
Notes: Sources: FCC Title 47, Chapter I, Subchapter A, Part 15 -> eCFR :: 47 CFR Part 15 -- Radio Frequency Devices

## Slide 6
EMI Filter – General Strategy
Ideally, prevent noise from coupling into system at source.
  Reduce parasitic inductance, capacitance
  Easier said than done
Failing that, use a filter at the device input to prevent as much noise from leaving the appliance as possible.
  Filters for CM and DM noise can be (mostly) designed separately.
  The noise source has an impedance and the LISN also has an impedance, EMI filter should mismatch impedances to attenuate the noise as much as possible.
So, need to have an idea as to the impedance of the noise source to effectively design an EMI filter.
  Noise impedance is:
    Non-ideal
    Frequency dependent.
    Electrical Circuit Dependent
    Appliance Geometry Dependent
Notes: Sources: FCC Title 47, Chapter I, Subchapter A, Part 15 -> eCFR :: 47 CFR Part 15 -- Radio Frequency Devices

## Slide 7
Determining Noise Source Impedance – Series Insertion
Baseline Measurement
  Don’t really have a good way to measure directly, LISN will let us measure * though!
  Establish Baseline
  Insert a series impedance and find
  Attenuation can be expressed as the ratio of these values
  Simplify…
  So, what’s the fuss? seems to be trivial to solve for…
  Actual expression is little less nice
Series Impedance Measurement
Spectrum Analyzer only lets us measure …
Purple: Vs
Orange: Voltage divider of Vnoise

## Slide 8
Determining Noise Source Impedance – Series Insertion
Baseline Measurement
  Absolute value means we lose the phase of the noise source impedance, and only know the min and max of the magnitude
  If we absolutely need one “nominal” value, the best estimate (lacking phase) is the geometric mean
Series Impedance Measurement

## Slide 9
Determining Noise Source Impedance – Shunt Insertion
Baseline Measurement
  A similar method using a shunt impedance insertion can be used for
Shunt Impedance Measurement

## Slide 10
Determining Noise Source Impedance – Summary
Baseline Measurement
Knowing the noise source impedance allows us to calculate a nominal attenuation for our filters
  Caveats
    Only have a range for source impedance magnitude
    Don’t know the source impedance phase
    Source impedance is frequency dependent, likely won’t have good data spanning the entire frequency range
  Assumptions will have to be made!
    Calculated attenuation will only give rough idea of real world performance
Shunt Impedance Measurement

## Slide 11
Example – PTW600

## Slide 12
Baseline Measurements
Notes: Remember to include noise floor… Talk about why peak measurements were taken? EMI specific measuring stuff?

## Slide 13
Series Measurement
Need to be above noise floor
Parallel resistors is a handy trick to degrade the performance of a choke.

## Slide 14
Shunt Measurement

## Slide 15
CM Source Impedance Calculation
Only have “real” data across subsection of spectrum.
Need to pick reasonable values to fill the entire spectrum
is skewed by outliers
seems to work well

## Slide 16
DM Source Impedance Calculation
Got more consistent results with using for entire spectrum

## Slide 17
Choke Impedance Curve
Outliers here can probably be ignored
Lower Frequencies are of more interest for this chart
3.78k
2.12k
Sample Choke - Wurth

## Slide 18
Current Production – No Choke
Peak
Avg
QP

## Slide 19
Original Design – With Choke

## Slide 20
New Design

## Slide 21
Abel Keeley
Electronics EEDP | Clothes Care
GE Appliances, a Haier company
Thank You

## Slide 22: Sources

## Slide 23
Python Design Tool Walkthrough

## Slide 24
Measurement File Select
Frequency [Hz] | Common Mode Baseline Data [dBm] | Common Mode Filtered Data [dBm] | Noise Floor Data [dBm] | Differential Mode Baseline Data [dBm] | Differential Mode Filtered Data [dBm]
150000 | -26.98616 | -29.76937 | -50.23812 | -25.81429 | -24.72054
154500 | -24.69612 | -34.86702 | -49.47151 | -27.70394 | -25.84358
159000 | -24.84261 | -28.74886 | -50.02815 | -27.41585 | -25.29671
Example of what a measurement file should look like. Selecting view template will create a CSV file with the correct headers that you can copy your measurements into.
Note – the frequency should typically run from 150KHz to at least 30MHz. For every given frequency, there must be a measurement in every column.

## Slide 25
Noise Impedance
Example of what choke model file should look like. The tool will perform linear interpolation between the provided data points, so make sure you have enough data points to provide a reasonable accurate interpolation. Selecting Generate Template will create a CSV file with appropriate headers for you to fill out.
Note – the choke and capacitance numbers should reflect the actual components you used to gather the initial data with. You NEED TO TEST THOSE EXACT COMPONENTS.
Frequency | Impedance
150000 | 636.2688
154500 | 620.0379
159000 | 604.7257
163500 | 590.2564
168000 | 576.5623
Check the data visualizations here to make sure they make sense. For finding source impedance, any measurements near the noise floor will be thrown out!

## Slide 26
CM Filter Design
Pretty self explanatory. Enter what margin you want from the filter, and what Y cap will be used. The Min Impedance Curve will show an estimate of the minimum impedance needed from CM choke to pass conducted emissions with the desired margin.
Note – This tool assumes the CM filter will be an LC filter. Maybe this will be changed down the road?
The min impedance curve can be saved to CSV for future use. Really want to focus on frequency ranges where the appliance performs worst, as those are ranges where we both have the best data and have the most room for improvement.
The estimated performance of a given choke can be seen.

## Slide 27
DM Filter Design
Similar to CM Design, but this time we are specifying CM choke leakage, and finding a maximum impedance curve for the X cap.
Note – This tool assumes the DM filter will be a Pi filter taking advantage of the CM choke’s leakage and the Y Caps. Changing the choke and/or the Y caps will thus affect the DM performance.
The estimated performance of a given capacitor can be seen.